## Slide 1
How to use the NAHB Powerpoint template
Custom Slide (Slide 1 of this template)
This slide is for use when the headline or content does not fit the existing options. This slide has the text box and arrow element placed (rather than embedded in the master slides) so that it may be enlarged or adjusted as necessary.
Title Slide (Slide 3 of this template)
Title pages should be simple and include just the title (and optional subhead) with the arrow and dots element. The red/blue arrow graphic is supplied for the title pages. If you are using a subhead, it should be half the size of the title type, right justified, Calibri Italic and the dark blue (from the corporate palette).
Section Slides (Slide 4-6 of this template)
Section Slides are used to divide large sections of content. These slides should be used at the beginning of each section. Full bleed backgrounds examples are also provided in this template. The circular “placeholders” are drag and drop. Simply drag your photo onto the circle and it will auto-crop to the circle. You may then use the cropping tools to better position your photo.
Please Note: For full bleed images, the drag and drop feature is not available. When rendering type over an image, a background “filter” or screen should be used. This template provides and example of this in use. To change the photo, you must go to the master slide, temporarily move the filter away, right-click on the photograph, and replace the image. Once you have replaced the image, move the filter back into position so that your type will be legible.
Divider Slides (Slide 7-8 of this template)
Divider slides are very similar to Section Slides and operate the same way. Divider slides are to be used to divide sections into subsections.
Content Slides (Slide 9-13 of this template)
Content slides will be used for the majority of content displayed on a presentation. There are multiple master page options with drag and drop image placeholders available. Full bleed artwork is not recommended on content slides. Color background is acceptable on content slides. Blue is provided on this template, but other colors from the palette are acceptable. However, if colors are changed, the arrow and dots graphic will need to match according to brand guidelines.
Ending Slide (Slide 14 of this template)
This slide is to be used at the end of each section and again at the end of the presentation. The colors provided are the recommended color palette for this slide.
Overall
Some adjustment of arrow size, placement of content, etc… is expected. This template is simply a beginning tool to use for creation of your presentations. Images should be pulled from the image library on Brandshare. If an appropriate image is not available, please contact marketing and request appropriate imagery. For more complex presentations, please contact marketing for assistance in the creation of the presentation.
Please make sure you are using the correct logo on all of your slides. The primary NAHB logo with descriptor is supplied. The logo may appear in the bottom left or right corner only. The logo may be in color, white, or the dark grey from the corporate palette. Never in black.
Upon creation of your presentation, please remove the instruction slide of this template (slide 1).

## Slide 2
Residential Streets

## Slide 3
Factors that Influence Street Design
Safety
Efficiency of Service
Livability
Economy
Notes: Principles derived from these factors:
  Local streets should be designed to discourage excessive speeds
  Land area devoted to streets should be minimized
Single most important feature of residential street design – the ability for traffic moving in opposite directions to share a single travel lane.
Streets are a significant element in total housing construction costs and also impact the environment – notably vegetation and stormwater runoff.
The traffic characteristics of residential streets and their construction, maintenance and performance requirements differ significantly from arterial and collector roads.

## Slide 4
Streets Serve Many Purposes
Direct auto access for residents
Carry traffic
Visual setting
Entryway for each house
Pedestrian/bicycle circulation system
Meeting place for residents
Play area for children
Shape neighborhood design
Notes: In the past, residential streets have been mistakenly viewed as fulfilling only 3 functions: providing access, providing on-street parking, and conveying traffic. As a consequence, guidelines placed undue stress on the efficient movement of traffic (on moving traffic in greater volumes or at increased speed). This overshadowed the need to balance cars and people.
To design and engineer streets solely for the convenience of easy automobile movement overlooks the many overlapping uses of a residential street.

## Slide 5
Principles of Street Planning
Street planning should relate to overall community planning, including pedestrian and bicycle activity
Traffic in residential areas should be kept to a minimum
The street is an important component of overall residential community design.
Street design standards should permit flexibility in community design. They should allow street alignments to follow natural contours and preserve natural features or to respond to other design objectives such as the creation of urban or village scale streetscapes.
Notes: Everyone benefits from streets that are functionally adequate, durable, and cost-effective as well as well-designed. Home buyers want streets that are safe and functional yet provide an attractive residential environment.
Streets are a particularly visible element within a residential setting and their design and appearance can greatly enhance or retract from a community. The movement of vehicles is only one of a streets many functions.

## Slide 6
Principles of Street Planning
5. Street pavement layouts should be planned to avoid excessive stormwater runoff and avoid heat buildup.
6. Streets can function socially as meeting places or centers of community activity.
7. In the interest of keeping housing affordable, street costs should be minimized.
8. Different streets have different functions and need to be designed accordingly. Blanket guidelines are inappropriate.
Notes: Properly scaled residential streets can create more attractive communities and can contribute to a clearly defined sense of place.
These principles suggest that a street system should be designed as a hierarchy of street uses.

## Slide 7
Design Considerations
Natural features of the site
Connection points
Preliminary idea of the lot plan
Cross-section features
  Number of lanes
  Type of drainage
  Pavement width
  Sidewalk placement
  ROW needed to contain street elements
Longitudinal Features
  Horizontal alignment
  Vertical profile
  Gradient
Notes: The design process begins with the layout of the street system.

## Slide 8
Street Hierarchy
Arterial Street
Residential Collector Street
Local Street
Cul-de-sac
Notes: The primary purpose of arterial streets in mobility – the movement of as much traffic as possible at as high a speed as possible.
The function of residential collector streets is a balance between mobility and access. They serve as a link between arterial streets and local streets.
Local streets are provided predominantly for access to the residential properties that front them.
A cul-de-sac is a local street that provides no outlet or connection with other streets.
In this presentation we will be focusing on residential collector and local streets.

## Slide 9
Residential Collector Streets
Link between local streets and arterial streets
Fronted by active properties – typically businesses, institutions or multifamily residences
Make up 5 to 10 percent of the total street mileage in new development
Ideally, no residential location is more than one-half mile from a collector street
Notes: Properly designed residential collector streets can have high value as frontage for both residential uses and small-scale neighborhood commercial uses.

## Slide 10
Local Streets
Provided predominantly for access to the residential properties that front them.
Account for 90% of the street mileage in new communities.
Notes: A major distinction between local streets and residential collector streets revolves around parking. Local streets allow parking even if doing so reduces the street to a single moving lane. The parking on residential collector streets must leave two unobstructed moving lanes to accommodate greater traffic volumes.

## Slide 11
Cul-de-sacs/Dead End Turnarounds
Circular Turnaround – preferable on most dead-end streets
T or Y Shaped Turnaround – May be used for streets having a short length, alleys, and streets serving up to 10 houses
No turnaround – extremely short streets serving no more than 5 houses. Vehicles may simply use street widths for backing/turning movements

## Slide 12
Street Network Types
The two most common types of street networks found in the united states are grid networks and “loops and lollipops”.
Grid – short block lengths, straight streets, back alleys. Higher level of connectivity with many route choices
Loop and lollipop –limit vehicular traffic, increased children's safety, less overall street area.
Hybrid networks – Desire for a neighborhood pattern where residents attain the qualities associated with dead-end streets and the connective qualities associated with the grid.
  The modified grid, in which some cross streets are replaced with paths, can include longer distances for vehicles than for pedestrians and bicycles.
  Circulation networks – houses are served on one side by vehicular access and on the other by pedestrian access.
Notes: The grid system has seen a revival in community design over the past two decades through the traditional neighborhood design movement (TND). This form of street design creates shorter blocks and more connections and therefore is more pedestrian friendly than the loop and lollipop network type. The grid patterned streets often have alleyways which provide service and parking at the rear of the building, eliminating the front loading garage.
Loop and lollipop networks are derived from the superblock design for Radburn, New Jersey, one of the first master planned communities. That plan was intended to create a residential environment that separated pedestrian and vehicular traffic with an internal park and walkways system and an external, or perimeter, roadway system.
A hybrid network is the next wave in street pattern experimentation.

## Slide 13
Access to Adjacent Street System
Multiple access points make possible alternative routes and this offers several advantages:
  Reduced congestion and internal travel volumes
  Diffusion of the development’s traffic impact on the external road system
  Continuity in the internal system for emergency and delivery services and for snow plows and other maintenance vehicles
Advantages of single access point include:
  Elimination of through traffic
  Increased security
Notes: Opinions differ as to whether residential areas should have several entrances from arterial or collector streets.
Entrances to residential areas from arterial or collector streets should be designed to allow access without encouraging through traffic.

## Slide 14
Design Speed
The following design features affect speed:
  Open width or clearance of the street
  Horizontal curvature
  Sight Distance
  Number of access points to the street
  Number of parked cars and other traffic calming devices
  Signs and signals at controlled intersections
Notes:   Open width or clearance of the street – A street with wide lanes invites higher speeds. As does a street with no visual obstructions within the ROW, enabling the driver to see over long distances.
  Horizontal curvature – The longer the radius of a curve, the higher the speed of that curve.
  Sight Distance – The straighter and more level the streets are the longer their sight distances
  Number of access points to the street – The presence of many obvious potential conflict points on streets tend to inhibit speeding.
  Number of parked cars and other traffic calming devices – The presence of parked cars and other potential obstructions effectively decreases traffic speeds.
  Signs and signals at controlled intersections – Traffic control devices slow traffic within the immediate vicinity of controlled intersections.

## Slide 15
Traffic Circles and Roundabouts
Traffic circles and roundabouts have been enjoying a resurgence in popularity in residential street design.
Roundabouts are larger and require more street space and the intersecting streets are flared as they approach the roundabout and triangular channelizing islands are centered in each connecting street
Traffic circles and roundabouts are generally safer than intersections controlled by stop signs or traffic signals.
Notes: Intersection traffic circles on local streets are usually small – 15 to 20 feet in diameter – and installing them in a normal four-way intersection requires no additional street space.
Two factors account for their safety:
  Curvature of the vehicle path reduces vehicle speed
  Likelihood of broadside or head-on collisions is greatly reduced.
The capacity of roundabouts and traffic circles exceeds that of intersections controlled by stop signs and traffic signals.

## Slide 16
Designing for Pedestrian and Bicycle Access
Good residential street design in itself accommodates bicycle travel as well as motor vehicle travel.
Examples of when a collector street may require bicycle lanes include:
  The street carries a significant portion of the developments total traffic
  Network of local streets is incomplete, forcing bicycle traffic onto the collector street as the only available route through the community
  Destinations for purposeful bicycle travel are nearby (schools, shopping)
  The subdivision is able to connect to an exterior system of bicycle trails and the subdivisions bicycle lanes provide an important link to the regional system
Notes: The backbone of a good bicycle network in a community is a well connected network of local streets.
Today’s emphasis on comprehensive community planning has made sidewalks, pedestrian ways, and bicycle paths an integral part of residential land development.
On residential collector streets, it may be appropriate to add on-street bicycle lanes.

## Slide 17
Designing for Pedestrian and Bicycle Access
Three –five foot border area between the sidewalk and the street provides many benefits including safety for children walking and playing, temporary storage for trash receptacles, and an area to store snow plowed off roadways.
Paved paths that may not strictly follow the grade or alignment of the street offer an option to traditional sidewalks.
Path sharing by bicycles and pedestrians is appropriate, particularly if the paths loop through the subdivision and are not used by through traffic.
Notes: In general, sidewalks should be provided on both sides of the street. Where side slopes are steep or historic areas exist, sidewalks on one side of the street may be appropriate. This may also be the case for large lot developments where frontages exceed 150 feet.
No special modifications need to be made to well-designed local and access streets in order to fully accommodate bicycles.

## Slide 18
Recommended Pavement Widths
Street Type | Pavement Width
Local Streets | 
No Parking Expected | 18 Feet
Low or Restricted Parking | 22-24 Feet
Normal Residential Parking | 24-26 Feet
Residential Collector | 32-36 Feet
Notes: In general, sidewalks should be provided on both sides of the street. Where side slopes are steep or historic areas exist, sidewalks on one side of the street may be appropriate. This may also be the case for large lot developments where frontages exceed 150 feet.
No special modifications need to be made to well-designed local and access streets in order to fully accommodate bicycles.

## Slide 19
Right-of-way Widths
The width of ROW is often mandated by ordinance.
ROW should only be as wide as necessary for the street pavement and other facilities and uses, including sidewalks, utilities, drainage, street trees, snow storage, and grading.
Notes: When public ROW includes sidewalks and bike paths, it needs to be wide enough to accommodate these uses.
Another option is to locate sidewalks and bike paths on land owned by the community association rather than in the ROW.
Many jurisdictions require the removal of all trees within a very wide ROW. Such a practice results in a great loss of trees and an increased expense in clearing. Limit the width of ROW to only what is necessary for safety and clearing trees only within 3-5 feet of the pavement edge are design practices that can yield substantial benefits by helping to create a more attractive community.

## Slide 20
Emergency Vehicle Access
Street pattern should provide at least two routes to any street within the community.
Establishing no-parking areas on some of a narrow street’s frontage can open up space for vehicles to pass and for setting up emergency equipment.
Parking can be eliminated on one side of streets that are frequently congested.
Notes: The most confining street situation for emergency vehicles is the local street with cars parked on both sides. The parked cars occupy 13-14 feet of the roadway, leaving 10 – 13 feet for the passage of emergency vehicles, even on a minimal 24-26 foot wide street.
Should emergency vehicle access become a problem on small residential streets, a variety of operational measures (in lieu of wider streets) can provide relief.

## Slide 21
Skinny Streets
Skinny Streets program created in Portland reduced minimum residential street widths to 20-26 feet
Queuing Street – A version of a skinny street where one travel lane serves traffic flowing in both directions
Possible to reduce impervious surfaces by 28% using a skinny street design. Also contributes to overall land use efficiencies and creates a more intimate feel.
A wide street also lacks the intimate scale that makes an attractive setting for housing.
Notes: Residential street standards dating back to the 1960s typically called for 50-60 foot right of ways with 34-36 feet of pavement. Not only do these streets use a lot of land and add excessive amounts of impervious surface, but they also encourage unsafe speeds. In recent years, these problems have been confirmed by national street standards associations that have recommended that streets be as narrow as 22 feet if they serve neighborhoods that produce low traffic volumes. – Skinny Streets and Green Neighborhoods by Cynthia Girling and Ronald Kellett
Portland, Oregon has a good example of a skinny street ordinance.

## Slide 22
Skinny Streets

## Slide 23
Traffic Calming Measures
Most traffic calming is achieved in one of three ways:
  Narrowing the width of the street or their apparent width to drivers
  Reducing site distances with curves
  Adding texture to the driving surface
Notes: Most traffic calming is achieved in one of three ways:
Narrowing the width of the street or their apparent width to drivers
Reducing site distances with curves
Adding texture to the driving surface
Pavement sharing is perhaps the single most powerful traffic calming measure that can be designed
A wide street also lacks the intimate scale that makes an attractive setting for housing.
Other elements of good street design can reinforce the sense of a narrow street, including curb and gutter drainage, uniform planning of street trees as close as possible to the pavement edge, and the occasional presence of parked vehicles.
Streets designed with curves and also grades that follow the natural contours of the terrain will have will have reduced sight distances which help to lower speeds.
Installing textured pavements at important areas, such as pedestrian crosswalks, is a traffic calming measure that can be built into the design of a community.

## Slide 24
On-Street Parking
Three options for on-street parking
  Parking on the side of the street
  Parking on both sides of the street
  Parking allowed only in parking bays provided at the edge of the street
On streets without curbs, an eight-foot improved shoulder can be used in lieu of paved parking lanes. Such shoulders can reduce the rate of stormwater runoff and may also help create a natural or rural appearance.
Where continuous on-street parking is impossible, angle parking at selected locations along the street may be suitable

## Slide 25
Public vs. Private Streets
Residential streets can be public or private
Public
  Developers dedicate them to the local government upon completion or , sometimes, after one year has passed.
  The local government then has the responsibility for maintaining the streets.
Private
  HOA or community association owns and maintains some or all of the streets as private streets.

## Slide 26
Streetscape
Paying attention to the aesthetics of the streets helps assure that they do not become simply thoroughfares for vehicles.
For example, much of the character of older neighborhoods is derived from the mature street trees that form a canopy over the entire street. By contrast, a neighborhood with wide streets devoid of trees conveys an entirely different image.
The placement of utilities and the style of traffic control devices and street-lighting hardware also contribute to the character of the street.
The location of above-ground utility structures should be coordinated with the proposed landscape plans.
Light poles and fixtures should relate to the architectural styles and character of the housing.
Signs – The design of Regulatory and warning signs (ex: “Stop”, “Curve”) are standardized, however, guide signs and recreational signs allow for some design individuality.
Notes: Paying attention to the aesthetics of the streets helps assure that they do not become simply thoroughfares for vehicles. For example, much of the character of older neighborhoods is derived from the mature street trees that form a canopy over the entire street. By contrast, a neighborhood with wide streets devoid of trees conveys an entirely different image. The placement of utilities and the style of traffic control devices and street-lighting hardware also contribute to the character of the street.
Choice of Plants – Consult with an urban forester, arborist or landscape architect. Consider mature height, spread, and maintenance requirements as well as the root systems potential for damaging sidewalks and street pavement.
Branches should be high enough to allow commercial vehicles to pass under
All trees and shrubs should allow clear site distance providing visibility for cars and trucks.
Careful planning allows for the incorporation of existing trees and shrubs. Vegetation need not be cleared from the entire ROW, but only as needed to accommodate utilities, drainage, etc.

## Slide 27
Streets as a Drainage System
In a closed drainage system, runoff is collected and retained within the roadway by curbs and gutters that convey the flow to the main drainage system.
Open drainage systems encourage infiltration of stormwater into the soils. Water is conveyed to swales and adjacent lawns or retention areas

## Slide 28
Alleys
Alleys provide alternative vehicular access to homes.
They can be particularly effective in reducing driveway entrances to the street, increasing the amount of on-street parking spaces available, improving the streetscape and avoiding home designs that present the garage as a dominant feature.
Notes: Off-street parking minimizes the need for parking on the street
Also keeps street clear for wide vehicles
To use land efficiently, alleys should be designed for the passage of a single service vehicle. A 12 ft pavement width with a 16 ft row will accommodate an 8 foot truck body with room to spare.

## Slide 29
What Can Builders Do to Increase Flexibility in Street Design
Work with the local planning department to incorporate more up to date standards
Include the local fire chief and provide examples of where these principles have worked
Incorporate innovative design and community benefits into your plan
Notes: Resources
Kulash, Walter M. Residential Streets, Urban Land Institute, Washington, D.C., 2001.
Girling, Cynthia and Ronald Kellett. Skinny Streets & Green Neighborhoods: Design for Environment and Community, Island Press, Washington D.C., 2005.
Southworth, Michael and Eran Ben-Joseph. Streets and the Shaping of Towns and Cities, Island Press, Washington, D.C. 2003.

## Slide 30
Complete Streets

## Slide 31
What are Complete Streets?
Complete Streets place an emphasis on alternative modes of transportation being incorporated into the streetscape and design.
Alternative transportation may include bike lanes, sidewalks, bus lanes and in very dense areas, light rail and streetcars.
On street parking and wider sidewalks are intended to encourage greater pedestrian activity and promote slower traffic movements.
Notes: With the growth in mixed-use and infill development, it is not a surprise that communities should look at making greater investments in transportation designed for walkable, higher density development.
As the builders of all residential units, from single-family all the way to high density multi-family, the home building industry has a vested interest in all policy aspects of the built environment, including the components being promoted within the Complete Streets movement.

## Slide 32
Components of a Complete Street
Landscaping
“Hardscape” – benches, lampposts, civic spaces
Accessibility – ramps, mats
Transit – Bus stops, Bus lanes, pull outs, light rail tracks
Bicycles – Bike lanes, Bike share facilities
Pedestrians – Sidewalks, Bump outs
Mixed – Use – Commercial and residential together
Connectivity – Multiple entrances, minimum block lengths, prohibited cul-de-sacs and multiple intersections
Notes: These components typically include:
Landscaping
“Hardscape” – benches, lampposts, civic spaces
Accessibility – ramps, mats
Transit – Bus stops, Bus lanes, pull outs, light rail tracks
Bicycles – Bike lanes, Bike share facilities
Pedestrians – Sidewalks, Bump outs
Mixed – Use – Commercial and residential together
Connectivity – Multiple entrances, minimum block lengths, prohibited cul-de-sacs and multiple intersections

## Slide 33
Concerns with Complete Streets
Often times local residential streets do not have the traffic levels needed to comply with complete streets programs but communities attempt to include them anyway
Complete Streets often incorporate lavish landscaping and hardscaping which can add cost to a project
Developers could be required to dedicate off-site improvements as part of a complete streets program that are much more expensive than conventional roadway improvements
Requiring connections within new developments into existing communities can create heavy NIMBY resistance to new development
Can lengthen the approval process and add cost, which can lead to an increase in housing costs
Notes: Complete Streets should be implemented as part of a comprehensive strategy that begins with the densest areas of a community and is then expanded to other areas as the network grows. Requiring developers to implement complete streets in all new developments, including those not connected to a complete streets network, is an onerous requirement. Suburban developments tend to be low traffic and include sidewalks, lessening the need to them to include many of the complete streets components. It is only the Residential Collector streets that would benefit from these enhancements, not local streets.
Re-zoning to mixed-use should only be considered when the market realities dictate that such a use is feasible economically.
Extra costs to implement a Complete Streets program should not be transferred to the building industry as a condition for development approval. This is an ongoing concern of the building industry, given the increased costs of off site infrastructure dedications that have already been born by the housing industry.

## Slide 34
Conclusions on Complete Streets
We support the communities interests in providing for more transportation options, or for pedestrians, cyclists and transit users to enjoy a secure and user –friendly environment. However, we do have concerns with the Complete Streets concept.
Therefore, we would like to reiterate areas that should be considered. A balanced approach to this issue will ensure a more varied and inclusive community that appeals to all residents and home buyers.
Notes: For more information on Complete Streets visit completestreets.org

## Slide 35
Green Streets

## Slide 36
What is a Green Street?
Urban transportation right-of-ways integrated with green techniques are often called “green streets.”
A Green Street is a sustainable stormwater strategy that meets resource protection goals by using a natural systems approach to manage stormwater, reduce flows, improve water quality and enhance watershed health.
Green Streets manage stormwater runoff, enhance community and neighborhood livability, and strengthen the local economy.
Notes: Green Streets mimic natural conditions by using soil and vegetation to manage runoff on the surface, at the source.
They can be attractive neighborhood amenities, and a variety of plants can provide a range of visual scened.
They are a subset of Low-Impact Development, an approach to land development (or re-development) that works with nature to manage stormwater as close to its source as possible.

## Slide 37
What are the Benefits of Green Streets?
Reduce impervious surface so stormwater can infiltrate to recharge groundwater and surface water;
Reduce polluted stormwater entering rivers and streams;
Divert stormwater from the sewer system and reduce basement flooding, sewer backups and combined sewer overflows;
Reduce demand on the city’s sewer collection system and the cost of constructing expensive pipe systems;
Increase urban green space;
Improve air quality and reduce air temperatures;
Address requirements of federal and state regulations to protect public health and restore and protect watershed health;
Increase community and property values; and
Improve pedestrian and bicycle safety
Notes: Transportation infrastructure, such as roads, parking lots and driveways, accounts for 55 to 75 percent of the existing impervious surfaces in our cities, towns and residential subdivisions.
These impervious surfaces do not allow rainfall to soak into the ground, where it would otherwise recharge underground aquifers.
These designs and practices are similar to the techniques traffic engineers use to achieve what they call “traffic calming.”
Green street practices can be built into the design of new residential projects or commercial streets and alleys, but they also can be used to retrofit existing streets and alleys to achieve similar results.

## Slide 38
What are the Various Components?
Alternative Street Designs (Narrower Street Widths)
Swales
Bioretention Curb Extensions and Sidewalk Planters
Permeable Pavement
Sidewalk Trees and Tree Boxes
Notes: The layout and street network must be planned to respect the existing hydrologic functions of the land (preserve wetlands, buffers, high-permeability soils, etc.) and minimize the impervious area. If retrofitting or redeveloping a street, opportunities to eliminate unnecessary impervious area should be explored.
Swales are vegetated open channels designed to accept sheet flow runoff and convey it in broad shallow flow.
Bioretention features can be tree boxes taking runoff from the street, attractive attention-grabbing planter boxes, or curb extensions.
Permeable pavement comes in four forms: permeable concrete, permeable asphalt, permeable interlocking concrete pavers, and grid pavers.
Most often street trees are given very little space to grow in often inhospitable environments. By providing adequate soil volume and a good soil mixture, the benefits obtained from a street tree multiply.

## Slide 39
SW 12th Avenue Green Street Project Portland, Oregon
Disconnects the street’s stormwater runoff from the storm drain system that feeds directly into the Willamette River and manages it on-site using a landscape approach.
Stormwater planters have the ability to reduce the runoff intensity of 25-year storm events by at least 70 percent.
Notes: Unique to Portland and the United States in the way the pedestrian zone of this street has been transformed to sustainably manage street stormwater runoff.
The landscape system within each planter allows the water to infiltrate into the soil at a rate of 4 inches per hour. If a rain event is intense enough, water will exit through the planter’s second curb cut, flow back out into the street and eventually enter the next downstream stormwater planter.

## Slide 40
Street Edge Alternatives (SEA) Streets Seattle, Washington
Reduced impervious surfaces to 11 percent less than a traditional street, provided surface detention in swales, and added over 100 evergreen trees and 1100 shrubs.
Two years of monitoring show that SEA Street has reduced the total volume of stormwater leaving the street by 99 percent.
Notes: Street Edge Alternatives (SEA) Streets are designed to provide drainage that more closely mimics the natural landscape prior to development than traditional piped systems.

## Slide 41
NE Siskiyou Green Street Portland, Oregon
This “green street” project carves out a portion of the street’s parking zone and converts it into two landscaped curb extensions.
Designed to elegantly capture, slow, cleanse, and infiltrate street runoff.
This street retrofit project demonstrates how both new and existing streets can be designed to provide direct environmental benefits and be aesthetically integrated into the neighborhood streetscape.
Notes: The NE Siskiyou Green Street project is unique to Portland and the United States in the way this quiet, 80 year-old residential street has been transformed to sustainably manage its stormwater runoff.
Because the NE Siskiyou Green Street Project was the first of its kind, the design, coordination, and permitting with other City Bureaus took almost a year to complete. Public outreach to the residents was extensive to assure acceptability and consensus. The effort has paid off in terms of widespread community acceptance. In fact, the City now has a waiting list of Portland residents who want similar landscaped stormwater facilities built on their own streets.

## Slide 42
Decatur Street, Edmonston, Maryland
New streetlights use efficient bulbs and ballasts, and are powered by an alternative source of energy (wind).
The street and sidewalk are accommodating to walkers, runners and bikers as much as possible
The materials used for the street and sidewalks themselves consist of as much recycled material as possible, including milled asphalt, concrete and glass.
Storm water, or rain runoff, is diverted away from storm drains and the sewer system to specially landscaped areas along the street, which filter the water naturally through the ground.
Notes: This is the first street of its kind in Maryland, and perhaps on the east coast.
All streets have an 'expiration date', a time when they must be repaired, resurfaced, or replaced. Instead of fixing their 'expired' streets in the conventional way, they fixed it in an environmentally responsible way.
The Mayor and Council enlisted a volunteer "Green Street Advisory Group" of residents, students, engineers, designers, and representatives from environmental and health organizations to generate ideas, review plans, and advise town officials on the project.

## Slide 43
The Builder’s Concerns with Green Streets
Green street practices can see opposition by local fire departments, public safety officials or traffic engineers, who oppose reducing street widths or modifying current standards for streets.
Permeable pavements for stormwater control can be more costly than impervious pavements and more difficult to install.
The long-term performance of LID stormwater devices is uncertain, including green street practices.
Opposition can arise from local residents who oppose measures that decrease parking availability on streets or alleys.
Notes: Installing devices such as vegetated curb extensions, sidewalk planters, vegetated swales and others may have long-term
issues since the devices must be maintained in perpetuity for a city or town to receive credit towards water quality mandates.
Some cities have initiated pilot programs, installing green streets at selected locations. These experimental designs serve as models for other cities hard pressed to find affordable ways to meet increasingly difficult and costly water quality goals.

## Slide 44
Questions?
Nicholas Julian
Program Manager, Land Use, NAHB
njulian@nahb.org
202-266-8309